www.wattstopper.com

800.879.8585

# Text boxes

## SPECIFICATIONS

#### WPIR

- The passive infrared sensor shall be capable of detecting presence in the control area, by detecting changes in the infrared energy.  Small movements shall be detected such as when a person is writing while seated at a desk.

- To avoid false ON activations and to provide high sensitivity to minor motion, Pulse Count Processing and Detection Signature Analysis shall be used to examine the frequency, duration, and amplitude of the signal received by the sensor to respond only to those signals caused by human motion.

- Sensor shall utilize mixed signal ASIC (application-specific integrated circuit) technology, which combines analog and digital processing into one chip package, to provide immunity to RFI and EMI.

- Sensor shall utilize a temperature compensated, dual element sensor and a multi-element Fresnel lens.

- Fresnel lens shall be a Poly IR 4 based material to offer superior filtering capability of competing light sources, such as the sun and other visible light sources. Lens shall have grooves facing in to avoid dust and residue build up which affects IR reception.

- Sensor shall have a 30 element Fresnel lens, 5 layers vertically and 6 layers horizontally, with a field of view of 110° vertically and horizontally.

- Sensor shall cover 300 square feet at normal mounting heights.

- Sensor shall have the ability to sense directly under and slightly behind sensor when mounted on ceiling.

- Sensor shall be capable of vertical or horizontal mounting with a 40 feet linear coverage in the vertical configuration.

- Time delay range shall be adjustable from 30 seconds to 30 minutes.

- Sensor shall have user-adjustable sensitivity setting.

- Sensor shall have in place a bypass pin which when removed will override sensor to ON and which requires no rewiring or modification to unit.

- Adjustments and mounting hardware shall be concealed under a removable cover to prevent tampering of adjustments and hardware.

- The sensor shall not protrude more than 1 1/4  inches from the ceiling (or wall) and should blend in aesthetically.

- Sensor shall be capable of being wired in parallel to allow coverage of large areas.

- To ensure quality and reliability, sensor shall be manufactured by an ISO 9002 certified manufacturing facility and shall have a defect rate of less than 1/3 of 1%.

- Sensor shall have standard 5 year warranty.

- Sensor shall be UL and CUL listed.

### WPIR Passive Infrared Occupancy Sensor

www.wattstopper.com

800.879.8585

WPIR1204