White Paper

New Generation of Floor Box Brings Innovation to all Types of Floor

For years, advances in the design of floor boxes have been incremental, with the result that many boxes on the market today are essentially the same as they were a generation ago. For example, up to now the selection of a box has been dependent on the type of floor in which it was to be installed. Further, once installed, boxes were difficult to relocate. Other floor box drawbacks that have not been fully addressed until now include insufficient space and capacity for audio/video and durable cable egress doors.

Legrand/Wiremold has introduced the industry’s most advanced series of floor boxes that offer high capacity and multi-functional capability for power, communications and audio/video. The Wiremold® Evolution™ Series Floor Box has unique design features that allow the same box to be installed in raised, carpet-covered concrete, terrazzo, polished concrete and wood floors without additional parts or accessories.

Design Innovations

Evolution Series Floor Boxes are available in 6-, 8- and 10-gang configurations for standard, on-grade and fire-classified applications. A furniture-feed box is also offered.

Fire classified Evolution Series Floor Boxes fit into a specially designed pan. When concrete is poured, a minimum of 3¼" of concrete surrounds the box itself. Wire and cable access is achieved through four 1¼" stems that feed – much like a poke-thru device – through the floor to the space below. These stems contain an intumescent material that expands during a fire and fills the space surrounding the cables.

In a feature unique to the Evolution Series Floor Box, the modules that support industry-standard single-, double-, and triple-gang device plates can be detached and removed through the top or back of the box. This allows for easier installation by multiple trades over different times during the construction cycle. The removable modules also facilitate moves, adds and changes to the box as services do not need to be entirely disconnected and reconnected. These modules also feature removable dividers and a tunnel feature that allows all compartments to be connected

The inside of the box, which is fully finished and painted white for better visibility, has ample work space in front of and behind device plates. A minimum of 3 1/2" of space is provided behind each device plate, allowing the box to accept A/V devices from all leading manufacturers. A minimum of 5" of space is provided between device plates for ample access when plugging into and unplugging from the devices. Integrated management guides keep cables organized and make it easier to feed them through the egress doors. Knockout sizes range from ¾" to 2". Knockout plates can be removed for even greater capacity.

Cover

The Evolution Series Floor Box cover features a patent-pending slide egress door system that locks into position when the box is open, but automatically closes around cables when the cover is shut. This feature protects cables and reduces potential trip hazards. The cover swings open a full 180 degrees and lies flat on the floor to provide easier access and guard against damage or trip hazards. Evolution Series Floor Boxes feature TopGuard™ protection, which exceeds UL’s scrub water requirements.

Evolution Series Floor Box covers are also designed for enhanced aesthetics. Low-profile, ADA-compliant covers are available in standard and flush styles with solid surfaces or large carpet cut-outs so they blend better with surrounding floor areas. These die-cast aluminum covers are available in black, brass, bronze, gray and nickel powder coat finishes.

# # #