SECTION 26 05 33.16

TABLE BOXES FOR ELECTRICAL SYSTEMS

GENERAL

CONDITIONS AND REQUIREMENTS

The General Conditions, Supplementary Conditions, and Division 01 – General Requirements apply.

SECTION INCLUDES

Table boxes for power, communications and A/V connectivity.

RELATED SECTIONS

Specifier Note:  In this article, specify work specified in other sections that is related to work of this section.

Section 07 84 13.16 - Penetration Firestopping Devices.

Division 26 - Electrical:  Electrical systems and components.

Division 27 - Communications:  Communications and audio-video systems and components.

Division 28 - Electronic Safety and Security:  Security systems and components.

Specifier Note:  The following paragraph is a sample that may be used in this article.  Add to or delete from the following as appropriate for the specific project.

Section [xxxxx] – [Section Title]:  [Include brief description of work specified in another section that is related to the work of this section.]

SUBMITTALS

Specifier Note:  In this article, specify various types of data to be furnished by the contractor before, during, or after construction. Topics included in this article are:  product data, shop drawings, samples, design data, test reports, certificates, manufacturers’ instructions, manufacturers’ field reports, qualification statements, and closeout submittals.

Submit under provisions of Section [01 33 00] [______].

Product Data:  Submit for table boxes.

Samples:  Submit [three (3)] [___________] with required color and finish.  Show standard color ranges available.

QUALITY ASSURANCE

Specifier Note:  In this article, describe qualifications, regulatory requirements, certifications, field samples, mock-ups, and pre-installation meetings.

Manufacturer Qualifications:  Firms regularly engaged in manufacture of electrical table boxes and fittings of the types and sizes required, whose products have been in satisfactory use in similar service for not less than 10 years.  Provide electrical table boxes and fittings produced by a manufacturer listed in this section.

Source Limitations:  Obtain each type of table box through one (1) source from a single manufacturer.

Electrical Boxes and Fittings:  Comply with requirements of applicable local codes, NEC, UL, ETL, and NEMA Standards pertaining to boxes and fittings.

DELIVERY, STORAGE AND HANDLING

Deliver table boxes in factory labeled packages.

Store and handle in strict compliance with manufacturer’s written instructions and recommendations.

Protect from damage due to weather, excessive temperature, and construction operations.

PRODUCTS

MANUFACTURERS

Basis-of-Design Product:  The design for table boxes and fittings is based on the Lab Bench Table Box manufactured by Legrand/Wiremold, 60 Woodlawn Street, West Hartford, CT 06110; toll-free 800-621-0049, telephone 860-233-6251, fax 860-232-2062; Web Site: www.legrand.us/wiremold.

Substitutions will be considered under provisions of Section 01 25 00.

TABLE BOXES

Classification and Use:  Table boxes shall have been examined and tested by Underwriters Laboratories Inc. to meet UL514A under File No. E2961 for Metallic Outlet Boxes and File No. E15191 for Multioutlet Assembly.  Table boxes are approved for use on table tops and lab benches and meet or exceed the UL111 spill water exclusion test.

Table Boxes, General:  Aluminum multi-service table boxes shall provide convenience outlets for power, data and A/V services.

Lab Bench Table Boxes:  Lab Bench Table Boxes; cULus Listed Metallic Outlet Boxes and cULus Listed Multioutlet Assembly; meets Article 380 of NEC and Article 12-3032 of CEC; evaluated for use on laboratory bench work surfaces.

Lab Bench Pedestal:  Part No. LBP2; aluminum housing and side plates with steel base and divider, measures 4" x 5" x 5-5/8" [102mm x 127mm x 143mm].  Base is configurable to have a combination of 2-3/4" knockouts or 3/4" EMT stubs.  Accommodates a variety of power outlets (duplex, decorator, GFCI and up to 30A twist lock).  Use Wiremold AVIP to provide communications and A/V.

Bottom Housing Unit:  Part No. LBPHA; one (1) gang 3/4" trade size conduit housing assembly.  Assembly includes junction box and 3/4" fitting to attach to 3/4" trade size conduit for power connections.

MAAP Plate:  Part No. LBP-MAAP; black finished plate to match Wiremold AVIP devices; provides communication and A/V services.

AAP Plate:  Part No. LBP-AAP; black finished plate to match Extron® Electronics AAP devices.

EXECUTION

EXAMINATION

Specifier Note: Retain one (1) of the options in the first paragraph below and delete the other one.

Examine conditions under which boxes and fittings are to be installed.  Notify the [Architect/Engineer] [Construction Manager] in writing of conditions detrimental to proper completion of the work.  Do not proceed with work until unsatisfactory conditions have been corrected.

INSTALLATION

Strictly comply with manufacturer's installation instructions and recommendations.  Coordinate installation with adjacent work to ensure proper clearances and to prevent electrical hazards.

CLEANING AND PROTECTION

Clean exposed surfaces using non-abrasive materials and methods recommended by manufacturer.

Protect boxes until acceptance.

END OF SECTION

A copyright license to reproduce this specification is hereby granted to non-manufacturing engineers, architects and specification writers.

|  | Legrand / Wiremold U.S. and International: 60 Woodlawn Street ( West Hartford, CT 06110 1-800-621-0049 ( FAX: 860-232-2062 ( Outside U.S.: 860-233-6251 Canada: 570 Applewood Crescent ( Vaughan, Ontario L4K 4B4 1-800-723-5175 ( FAX: 905-738-9721 |
| --- | --- |
| (2013 Legrand/Wiremold All Rights Reserved | EDXXXX – Updated July 2013 – For latest specs visit www.legrand.us/wiremold |