GUIDE SPECIFICATIONS

Wiremold®  3300 Series Raceway

al3300 Single-channel aluminum raceway

PART 1 GENERAL

1.1	Scope

This specification covers an aluminum surface metal raceway system used for branch circuit wiring and/or data network, voice, video and other low-voltage wiring. The aluminum raceway system shall consist of raceway, appropriate fittings and device brackets to complete the installation per the electrical, communication and/or laboratory equipment drawings.

1.2	Classification and Use

Aluminum surface metal raceway is to be utilized in dry interior locations only as covered in Article 386 of the National Electrical Code, as adopted by the National Fire Protection Association and as approved by the American National Standards Institute. The Wiremold Company AL3300 raceway system is listed by Underwriters Laboratories under File No. E73943 Guide RJBT and File No. E74243 Guide RJPR.

1.3	Submittals

1.3.1 Shop Drawings

For prewired installations, submit drawings for approval showing the complete layout of all products that make up the complete system for each floor prior to installation with raceway lengths, device type (power and data), locations and circuits identified.

1.3.2 As Built Drawings

If variations from approved shop drawings occur during the installation of the system, final, as built drawings, shall be submitted for each floor that has been altered.

PART 2 PRODUCT

2.1	Manufacturer

The aluminum surface metal raceway system specified herein for branch circuit wiring and/or data network, voice, video and other low-voltage wiring shall be the AL3300 System as manufactured by The Wiremold Company. Systems of other manufacturers may be considered equal if, in the opinion, and the written approval of the engineer, they meet all 
the performance standards specified herein. Manufacturers requesting consideration as an equal to The Wiremold system shall submit a list of similar installations in service for two (2) years or longer.

2.2	Materials

The raceway and all system components must be UL Listed in full compliance with their standard for surface metal raceways and fittings (UL-5). All extrusions are to be 6063-T5 aluminum alloy, with nominal wall thickness of 0.060" [1.52mm] throughout. The surface finish is to be #204R1 heavy etched Architectural Class II clear anodized finish.

2.2.1 Raceway

The raceway shall be a two-piece design with a base and snap-on cover. The base sections shall be furnished in 10' [3.048m] lengths and the cover sections in 5' [1.52m] lengths. The overall dimensions of assembled raceway shall be 2 7/8" [73.02mm] wide by 1 7/8" [47.62mm] deep with a cross sectional area of 4.40 square inches [2.839mm2]. A field-installed divider is available to separate the 2 7/8" [73mm] width into two equal but separate wiring compartments to handle both power and communications wiring.

2.2.2 Fittings

A full compliment of fittings for the raceway shall be available including, but not limited to, flat, internal and external elbows, tee and cross fittings, couplings for joining sections of raceway and transition connectors to 1/2" and 3/4" [12.7mm and 19mm] trade size conduit. Receptacle cover plates and an offset divider bracket are to be offered for mounting commercially available duplex devices in an in-line and offset configuration and, rectangular GFCI and Sentrex® surge receptacles. The fittings shall have a satin anodized finish to match the raceway.

2.2.3 Communication Devices and Accessories

The raceway manufacturer will provide a complete line of connectivity outlets and modular inserts for UTP/STP, Fiber Optic, Coaxial and other cabling types with face plates and bezels to facilitate mounting.  A complete line of preprinted station and port identification labels, snap-in icon buttons as well as write-on station identification labels shall be available.

PART 3 EXECUTION

3.1	Installation

Prior to and during installation, refer to system layout drawing containing all elements of the system. Installer shall comply with detailed manufacturer’s installation instruction sheets, 
which accompany system components, as well as, system instruction sheets, whichever 
is applicable.

3.1.1 Mechanical Security

All raceway systems shall be mechanically continuous and connected to all electrical outlets, boxes, and cabinets, in accordance with manufacturer’s installation sheets.

3.1.2 Electrical Security

All metal raceway shall be electrically continuous and bonded in accordance with the National Electric Code for proper grounding.

3.1.3 Completeness

Work shall include fastening all raceway and appropriate fittings and device plates to install a complete aluminum surface raceway system as indicated on the electrical, communication and/or laboratory equipment drawings in the applicable specifications. All raceway systems shall be installed complete, including insulating bushings and inserts where required by manufacturer’s installation sheets.

|  | Legrand U.S. and International: 60 Woodlawn Street ( West Hartford, CT 06110 1-800-621-0049 ( FAX: 860-232-2062 Canada: 570 Applewood Crescent ( Vaughan, Ontario L4K 4B4 1-800-723-5175 ( FAX: 905-738-9721 |
| --- | --- |
| (2005 Legrand All Rights Reserved | ED594R2 – Updated January 2005 – For latest specs visit www.legrand.us |